## Slide 1
BATTERY ENERGY STORAGE SYSTEM
PERMIT SET
GENERAL NOTES
1. ALL CONSTRUCTION SHALL COMPLY WITH THE CODES ADOPTED BY {{AHJ_CITY}} AS DESCRIBED IN THE {{MUNICIPAL_CODE}} INCLUDING BUT NOT LIMITED TO {{CODE_YEAR}} CEC, CFC & CBC. 2. BEFORE INITIATING ANY WORK, THE CONTRACTOR SHALL NOTIFY ENGINEER OF RECORDS OF ANY DISCREPANCIES IDENTIFIED ON EXISTING CONDITIONS, STRUCTURE, ELECTRICAL, ETC. 3. CONTRACTOR SHALL BE RESPONSIBLE FOR ALL SAFETY PRECAUTIONS, OSHA REQUIREMENTS AND SAFETY MEASUREMENTS ON SITE. 4. CONTRACTOR IS RESPONSIBLE FOR INSTALLING ALL EQUIPMENT AND FOLLOWING ALL MANUFACTURER'S OR ENGINEER'S DIRECTIONS AND INSTRUCTIONS. 5. CONTRACTOR IS ADVISED THAT ALL DRAWINGS, COMPONENT MANUALS, ESPECIALLY INVERTER MANUALS, ARE TO BE READ AND UNDERSTOOD PRIOR TO INSTALLATION OR ENERGIZING OF ANY EQUIPMENT. 6. CONTRACTOR IS RESPONSIBLE FOR SELECTING AND PURCHASING EQUIPMENT DESIGNED TO LAST A MIN. OF 30 YEARS IN CONJUNCTION WITH THE BESS SYSTEM. 7. ALL CONTRACTORS ARE REQUIRED TO PROVIDE FULL SUBMITTALS OF INTENDED ORDERS TO CLEARSKY FOR REVIEW. 8. WHENEVER ANY SURFACE IMPROVEMENTS SUCH AS PAVEMENT, CURBING, PEDESTRIAN WALKS, FENCING, OR TURFING HAVE BEEN REMOVED, DAMAGED, OR OTHERWISE DISTURBED BY THE CONTRACTOR'S OPERATIONS, THEY SHALL BE REPAIRED OR REPLACED TO THE PRE-EXISTING CONDITION. 9. REFILL AND RESTORE THE WORK AS DIRECTED, DURING CONSTRUCTION AND PRIOR TO PROJECT COMPLETION, TO MAINTAIN ACCEPTABLE SURFACE CONDITIONS. 10. ALL ADDITIONAL MATERIALS REQUIRED SHALL BE FURNISHED WITHOUT ADDITIONAL COST TO THE OWNER. 11. ANY WORK BEGUN PRIOR TO ATTAINING APPROVAL AND SIGNATURES OF {{AHJ_CITY}} WILL BE AT CONTRACTOR'S RISK, AND WILL BE STOPPED IF PRE-APPROVED BY PROJECT OWNER. 12. COORDINATE OPERATIONS WITH ALL REQUIRED MATERIALS TESTING SERVICES AS REQUIRED BY THESE DRAWINGS. 13. NOTIFY ALL UTILITY COMPANIES INVOLVED IN THE DEVELOPMENT PRIOR TO BEGINNING OF WORK. 14. COMPLY WITH ALL CURRENTLY APPLICABLE SAFETY LAWS OF ALL JURISDICTIONAL BODIES. 15. MAINTAIN CONTINUOUS TEMPORARY TRAFFIC BARRICADES, WITH OPERABLE FLASHING DEVICES, SPACED AT INTERVALS OF NOT TO EXCEED 50 FEET WHENEVER THE WORK AREA IS ADJACENT TO AN EXISTING TRAFFIC LANE. 16. ALL {{UTILITY}} REQUIRED EQUIPMENT SHALL BE INSTALLED IN ACCORDANCE WITH CURRENT {{UTILITY}} STANDARDS.
ELECTRICAL NOTES
1. THE LINE AND LOAD TERMINALS ON THE AC DISCONNECTS MAY BE ENERGIZED IN THE OPEN POSITION. SWITCH IS TO BE LABELED TO COMPLY WITH ARTICLE 690.17 OF THE NEC. 2. ALL WIRING SHALL CONFORM WITH THE LATEST EDITION OF THE NEC. ALL WIRING IS ASSUMED IN ACCORDANCE WITH THE NEC, UNLESS OTHERWISE LABELED. 3. GROUNDING OF THE BESS SHALL COMPLY WITH NEC 690.45 AND 690.47. 4. THE ELECTRICAL CONTRACTOR IS REQUIRED TO USE PERMANENTLY COLOR CODED INSULATION AND PROVIDE A COLOR CODE TO IDENTIFY DC AND AC CIRCUITS. 5. IN EVERY PULL BOX, TERMINAL BOX, AND AT ALL PLACES WHERE WIRES MAY NOT BE READILY IDENTIFIED BY NAMEPLATE MARKINGS ON THE EQUIPMENT TO WHICH THEY CONNECT, IDENTIFY EACH CIRCUIT WITH A PLASTIC LABEL OR TAG FOR NUMBER, POLARITY, OR PHASE. 6. FUSE CONDUIT SHALL ONLY BE USED WHERE SPECIFIED OR APPROVED IN WRITING. 7. THE GROUP-WIRING PROVISIONS OF THE NEC SHALL BE FOLLOWED FOR ALL CONDUCTORS PRE-ENGINEERED EXTENDED BATTERY ENERGY STORAGE. 8. THIS ELECTRICAL INSTALLATION IS TO BE CONSIDERED AN OPTIONAL STANDBY SYSTEM PER NEC 702. 9. THE {{BAT_MFR}} {{BAT_MODEL}} BATTERY STORAGE SYSTEMS ARE TO BE CONSIDERED PRE-ENGINEERED STATIONARY BATTERY STORAGE SYSTEMS.
ELECTRICAL ENGINEER
{{EE_NAME}}, {{EE_TITLES}}
{{EE_FIRM}}
{{EE_ADDR}}
{{EE_CITY_STATE}} {{EE_ZIP}}
PHONE: {{EE_PHONE}} FAX: {{EE_FAX}} EXT. {{EE_EXT}}
{{EE_EMAIL}}
STRUCTURAL ENGINEER
{{SE_NAME}}
{{SE_FIRM}}
{{SE_ADDR}}
{{SE_CITY_STATE}} {{SE_ZIP}}
PHONE: {{SE_PHONE}}
{{SE_EMAIL}}
PROPERTY OWNER
{{OWNER_NAME}}
{{OWNER_ADDR}}
GENERAL CONTRACTOR
{{GC_NAME}}
PO BOX {{GC_PO_BOX}}
{{GC_CITY}}, {{GC_STATE}} {{GC_ZIP}}
{{GC_EMAIL}} PH: {{GC_PHONE}}
LIC: {{GC_LIC}}
SCOPE OF WORK
THE PROJECT IS TO INSTALL NEW BATTERY ENERGY STORAGE SYSTEMS (BESS) AND ASSOCIATED ELECTRICAL EQUIPMENT. ALL CONSTRUCTION SHALL COMPLY WITH THE CODES ADOPTED BY {{AHJ_CITY}} AS DESCRIBED IN THE {{MUNICIPAL_CODE}} INCLUDING BUT NOT LIMITED TO {{CODE_YEAR}} CEC, CFC, CBC & OSHA. THE SYSTEM WILL BE INTERCONNECTED TO AND WILL BE OPERATING IN PARALLEL WITH THE ELECTRICAL UTILITY UNDER THE REQUIREMENTS OF {{UTILITY}} BY {{AHJ_CITY}} AT THE TIME OF PERMIT APPLICATION.
SHEET INDEX
E0
COVER SHEET
E1.0
PLOT PLAN
E1.1
ENLARGED PLOT PLAN
E1.2
DEMOLITION PLAN
E2.0
SINGLE LINE DIAGRAM
E4.0
SIGNAGE
S1.1
BESS PAD DETAILS
S1.2
GEAR PAD DETAILS
S2.0
GROUNDING DETAILS
S3.0
FENCING DETAILS
SITE INFORMATION
SITE LATITUDE
{{LAT}}
ZONING DISTRICT
{{ZONING}}
FLOOD ZONE
{{FLOOD_ZONE}}
EXPOSURE CATEGORY
{{EXPOSURE}}
SEISMIC DESIGN CATEGORY
{{SDC}}
RISK CATEGORY
{{RISK_CAT}}
WIND SPEED
{{WIND_SPEED}}
SNOW LOAD
{{SNOW_LOAD}}
BESS EQUIPMENT SUMMARY
PARAMETER
BATTERY CABINET
BATTERY INVERTER
BATTERY SNAPSHOT
MANUFACTURER
{{BAT_MFR}}
{{INV_MFR}}
{{BAT_MFR}}
MODEL NUMBER
{{BAT_MODEL}}
{{INV_MODEL}}
{{BAT_RACK_MODEL}}
QUANTITY
{{BAT_QTY}}
{{BAT_QTY}}
{{BAT_QTY}}
BATTERY BANK CAPACITY (kWh)
{{KWH}}
N/A
{{RACK_KWH}}
RATED VOLTAGE (V)
{{DCV}}
{{INV_AC}}
{{VOLTAGE}}
ENCLOSURE TYPE
{{NEMA_RATING}}
{{NEMA_RATING}}
{{NEMA_RATING}}
RATED OUTPUT CURRENT (A)
{{ACDIS}}
{{ACDIS}}
{{ACDIS}}
{{PERMIT_NO}}
REVIEWED FOR COMPLIANCE
{{AHJ_CITY}}
{{AHJ_DEPT}}
For {{PROJECT_NAME}} Subject to Code Compliance.
REVISIONS NEED REVIEW
☐ BUILDING CODE ☐ ELECTRICAL CODE
☐ MECHANICAL CODE ☐ PLUMBING CODE
☐ GRADING/DRAINAGE ☐ STRUCTURAL DESIGN
SPECIAL INSPECTION LIST
☐ FOUNDATION
☐ Grading and Drainage
☐ Piers and Caissons
☐ Shotcrete or Masonry
☐ CONCRETE
☐ Concrete Placement
☐ f'c = ___ psi
☐ Welding
☐ Reinf. Placement
☐ High Strength Bolting
☐ STEEL CONSTRUCTION
☐ SEISMIC
☐ FIRE RESISTANCE
☐ Structural Steel
☐ STRUCTURAL OBSERVATIONS (list below)
SITE CLEARING NOTES (IF APPLICABLE)
1. PROTECT FROM DAMAGE AND PRESERVE TREES, SHRUBS, AND OTHER PLANTS OUTSIDE THE LIMITS OF WORK AND WITHIN THE LIMIT OF THE WORK WHICH ARE DESIGNATED TO REMAIN UNDISTURBED. 2. REMOVE OBSTRUCTIONS, TREES, SHRUBS, GRASS AND OTHER VEGETATION TO PERMIT INSTALLATION OF NEW CONSTRUCTION. REMOVAL INCLUDES DIGGING OUT STUMPS AND OBSTRUCTIONS AND GRUBBING ROOTS. 3. FILL DEPRESSIONS CAUSED BY CLEARING AND GRUBBING OPERATIONS WITH SOIL MATERIAL APPROVED BY OWNER. 4. STRIP TOPSOIL WHERE REQUIRED. STOCKPILE IN AREA APPROVED BY OWNER. 5. WITH OWNER'S APPROVAL, REMOVE EXISTING ABOVE AND BELOW GRADE IMPROVEMENTS AS INDICATED AND AS NECESSARY TO FACILITATE NEW CONSTRUCTION. 6. DISPOSE OF REMOVED TREES, BRUSH, STUMPS, ROOTS AND ORGANIC DEBRIS IN A LEGAL MANNER OFF THE SITE.
ClearSky
BUILDERS LLC
PO BOX {{GC_PO_BOX}}
{{GC_CITY}}, {{GC_STATE}} {{GC_ZIP}}
PH: {{GC_PHONE}}
PN - {{PROJECT_NAME}}
{{SITE_ADDR}}
{{CITY_SHORT}}, {{STATE}} {{ZIP}}
APN: {{APN}}
{{PERMIT_NO}}
REVIEWED FOR COMPLIANCE
{{AHJ_CITY}}
{{AHJ_DEPT}}
For {{PROJECT_NAME}} Subject to Code Compliance.
REVISIONS NEED REVIEW
DATE
REV
COMMENTS
{{ISSUE_DATE}}
00
ISSUE FOR PERMIT
E0
COVER SHEET
ISSUE DATE
{{ISSUE_DATE}}
REVISION DATE
{{ISSUE_DATE}}
DESIGNED BY
{{DESIGNED_BY}}
CHECKED BY
{{CHECKED_BY}}
JOB NO.
{{JOB_NO}}

## Slide 2
E1.0 PLOT PLAN IMAGE (AI-enhanced site map from SiteMap Designer)
1 — PLOT PLAN · SCALE: 1" = {{PLOT_SCALE}}'
ClearSky
BUILDERS LLC
PO BOX {{GC_PO_BOX}}
{{GC_CITY}}, {{GC_STATE}} {{GC_ZIP}}
PH: {{GC_PHONE}}
PN - {{PROJECT_NAME}}
{{SITE_ADDR}}
{{CITY_SHORT}}, {{STATE}} {{ZIP}}
APN: {{APN}}
{{PERMIT_NO}}
REVIEWED FOR COMPLIANCE
{{AHJ_CITY}}
{{AHJ_DEPT}}
For {{PROJECT_NAME}} Subject to Code Compliance.
REVISIONS NEED REVIEW
DATE
REV
COMMENTS
{{ISSUE_DATE}}
00
ISSUE FOR PERMIT
E1.0
PLOT PLAN
ISSUE DATE
{{ISSUE_DATE}}
REVISION DATE
{{ISSUE_DATE}}
DESIGNED BY
{{DESIGNED_BY}}
CHECKED BY
{{CHECKED_BY}}
JOB NO.
{{JOB_NO}}

## Slide 3
E1.1 ENLARGED PLOT PLAN IMAGE (Auto-cropped BESS equipment area)
1 — ENLARGED PLOT PLAN · SCALE: 1" = {{ENL_SCALE}}'
ClearSky
BUILDERS LLC
PO BOX {{GC_PO_BOX}}
{{GC_CITY}}, {{GC_STATE}} {{GC_ZIP}}
PH: {{GC_PHONE}}
PN - {{PROJECT_NAME}}
{{SITE_ADDR}}
{{CITY_SHORT}}, {{STATE}} {{ZIP}}
APN: {{APN}}
{{PERMIT_NO}}
REVIEWED FOR COMPLIANCE
{{AHJ_CITY}}
{{AHJ_DEPT}}
For {{PROJECT_NAME}} Subject to Code Compliance.
REVISIONS NEED REVIEW
DATE
REV
COMMENTS
{{ISSUE_DATE}}
00
ISSUE FOR PERMIT
E1.1
ENLARGED PLOT PLAN
ISSUE DATE
{{ISSUE_DATE}}
REVISION DATE
{{ISSUE_DATE}}
DESIGNED BY
{{DESIGNED_BY}}
CHECKED BY
{{CHECKED_BY}}
JOB NO.
{{JOB_NO}}

## Slide 4
LEGEND
🟠 TREE TO BE REMOVED .............. {{BAT_QTY}}
⭕ TREE TO BE PROTECTED ............. {{BAT_QTY}}
E1.2 DEMOLITION PLAN IMAGE (Upload or auto-generated)
1 — DEMOLITION PLAN · SCALE: 1" = {{PLOT_SCALE}}'
ClearSky
BUILDERS LLC
PO BOX {{GC_PO_BOX}}
{{GC_CITY}}, {{GC_STATE}} {{GC_ZIP}}
PH: {{GC_PHONE}}
PN - {{PROJECT_NAME}}
{{SITE_ADDR}}
{{CITY_SHORT}}, {{STATE}} {{ZIP}}
APN: {{APN}}
{{PERMIT_NO}}
REVIEWED FOR COMPLIANCE
{{AHJ_CITY}}
{{AHJ_DEPT}}
For {{PROJECT_NAME}} Subject to Code Compliance.
REVISIONS NEED REVIEW
DATE
REV
COMMENTS
{{ISSUE_DATE}}
00
ISSUE FOR PERMIT
E1.2
DEMOLITION PLAN
ISSUE DATE
{{ISSUE_DATE}}
REVISION DATE
{{ISSUE_DATE}}
DESIGNED BY
{{DESIGNED_BY}}
CHECKED BY
{{CHECKED_BY}}
JOB NO.
{{JOB_NO}}

## Slide 5
SLD GENERAL NOTES
POINT OF INTERCONNECTION (POI) PER UTILITY REQUIREMENTS; SEE INTERCONNECTION AGREEMENT. ALL EQUIPMENT TO BE LISTED PER UL STANDARDS AND APPLICABLE BESS PER UL 9540; BATTERY MODULES PER UL 1973; INVERTERS PER UL 1741. ALL FIELD WIRING TO COMPLY WITH NEC {{CODE_YEAR}} (OR ADOPTED EDITION) — ART. 690, 705, & 706. CONDUCTORS SIZED PER ATTACHED CABLE / VOLTAGE-DROP SCHEDULE. ANTI-ISLANDING / RAPID SHUTDOWN PER UL 1741 SA / IEEE 1547-2018.
METER / SERVICE
Utility: {{UTILITY}}
Meter Number: {{METER_NO}}
Service Voltage: {{VOLTAGE}} / {{PHASE}} / {{FREQ}}Hz
Service Rating: {{ACDIS}}A AT MAIN
Existing AIC: {{KAIC}}
STORAGE NOTES
PROPOSED STORAGE DEVICE(S) WILL NOT EXPORT TO THE UTILITY GRID. SYSTEM IS CONFIGURED AS A NON-EXPORT, BEHIND-THE-METER ENERGY STORAGE SYSTEM USING UL-LISTED INVERTERS WITH NON-EXPORT CONTROLS. SYSTEM OPERATION SHALL COMPLY WITH UTILITY INTERCONNECTION AGREEMENT AND ALL APPLICABLE STANDARDS.
E2.0 SINGLE LINE DIAGRAM (Upload your SLD image)
CABLE SCHEDULE / VOLTAGE-DROP CALCULATIONS
CIRCUIT
FROM
TO
PHASES
VOLTAGE
CURRENT (A)
RUN (FT)
CONDUCTORS
GROUND
CONDUIT
VD %
METHOD
C1
BESS BANK 1
INVERTER 1
DC
{{DCV}}
{{ACDIS}}
{{FENCE_LEN}}
{{WIRE_AWG}}
{{WIRE_AWG}}
{{CONDUIT_SIZE}} EMT
{{PCT}}
NEC 310.16
C2
INVERTER 1
AC DISCO 1
3-PH
{{INV_AC}}
{{ACDIS}}
{{FENCE_LEN}}
{{WIRE_AWG}}
{{WIRE_AWG}}
{{CONDUIT_SIZE}} EMT
{{PCT}}
NEC 310.16
C3
BESS BANK 2
INVERTER 2
DC
{{DCV}}
{{ACDIS}}
{{FENCE_LEN}}
{{WIRE_AWG}}
{{WIRE_AWG}}
{{CONDUIT_SIZE}} EMT
{{PCT}}
NEC 310.16
C4
INVERTER 2
AC DISCO 1
3-PH
{{INV_AC}}
{{ACDIS}}
{{FENCE_LEN}}
{{WIRE_AWG}}
{{WIRE_AWG}}
{{CONDUIT_SIZE}} EMT
{{PCT}}
NEC 310.16
C5
AC DISCO 1
(N) SWITCHGEAR
3-PH
{{INV_AC}}
{{ACDIS}}
{{FENCE_LEN}}
{{WIRE_AWG}}
{{WIRE_AWG}}
{{CONDUIT_SIZE}} EMT
{{PCT}}
NEC 310.16
C6
XFMR SEC
AUX DISCO
3-PH
{{INV_AC}}
{{ACDIS}}
{{FENCE_LEN}}
{{WIRE_AWG}}
{{WIRE_AWG}}
{{CONDUIT_SIZE}} EMT
{{PCT}}
NEC 310.16
C7
AUX DISCO
AUX LOADS
3-PH
{{INV_AC}}
{{ACDIS}}
{{FENCE_LEN}}
{{WIRE_AWG}}
{{WIRE_AWG}}
{{CONDUIT_SIZE}} EMT
{{PCT}}
NEC 310.16
ClearSky
BUILDERS LLC
PO BOX {{GC_PO_BOX}}
{{GC_CITY}}, {{GC_STATE}} {{GC_ZIP}}
PH: {{GC_PHONE}}
PN - {{PROJECT_NAME}}
{{SITE_ADDR}}
{{CITY_SHORT}}, {{STATE}} {{ZIP}}
APN: {{APN}}
{{PERMIT_NO}}
REVIEWED FOR COMPLIANCE
{{AHJ_CITY}}
{{AHJ_DEPT}}
For {{PROJECT_NAME}} Subject to Code Compliance.
REVISIONS NEED REVIEW
DATE
REV
COMMENTS
{{ISSUE_DATE}}
00
ISSUE FOR PERMIT
E2.0
SINGLE LINE DIAGRAM
ISSUE DATE
{{ISSUE_DATE}}
REVISION DATE
{{ISSUE_DATE}}
DESIGNED BY
{{DESIGNED_BY}}
CHECKED BY
{{CHECKED_BY}}
JOB NO.
{{JOB_NO}}

## Slide 6
SIGNAGE REQUIREMENTS — PER NEC 706.15 AND IFC 1207
LOCATION: BESS QUANTITY: 1 TEXT: HEADER 34pt (0.472") SUB 18pt (0.25")
CAUTION:
THIS SERVICE SUPPLIED BY ALTERNATIVE POWER SOURCES WITH DISCONNECTS LOCATED AS SHOWN
E4.0 BESS SIGN MAP
LOCATION: MSB QUANTITY: 1 TEXT: HEADER 34pt (0.472") SUB 18pt (0.25")
CAUTION:
THIS SERVICE SUPPLIED BY ALTERNATIVE POWER SOURCES WITH DISCONNECTS LOCATED AS SHOWN
E4.0 MSB SIGN MAP
LOCATION: BESS ENCLOSURE (GREAT POWER)
ENERGY STORAGE SYSTEM DISCONNECT
LOCATION: BESS ENCLOSURE
ENERGY STORAGE SYSTEM
LOCATION: BESS ENCLOSURE (DYNAPOWER)
ENERGY STORAGE SYSTEM INVERTER
LOCATION: BESS ENCLOSURE
LITHIUM IRON PHOSPHATE TECHNOLOGY
LOCATION: BOLTSWITCH CABINET QUANTITY: 1
AC DISCONNECT BOLTSWITCH CABINET OPERATING CURRENT: {{ACDIS}}A OPERATING VOLTAGE: {{INV_AC}}V
LOCATION: XFMR QUANTITY: 1
ISOLATION XFMR XFMR SIZE: {{XFMR_SIZE}}KVA OPERATING VOLTAGE: {{V_PRI}}/{{V_SEC}}V
ClearSky
BUILDERS LLC
PO BOX {{GC_PO_BOX}}
{{GC_CITY}}, {{GC_STATE}} {{GC_ZIP}}
PH: {{GC_PHONE}}
PN - {{PROJECT_NAME}}
{{SITE_ADDR}}
{{CITY_SHORT}}, {{STATE}} {{ZIP}}
APN: {{APN}}
{{PERMIT_NO}}
REVIEWED FOR COMPLIANCE
{{AHJ_CITY}}
{{AHJ_DEPT}}
For {{PROJECT_NAME}} Subject to Code Compliance.
REVISIONS NEED REVIEW
DATE
REV
COMMENTS
{{ISSUE_DATE}}
00
ISSUE FOR PERMIT
E4.0
SIGNAGE
ISSUE DATE
{{ISSUE_DATE}}
REVISION DATE
{{ISSUE_DATE}}
DESIGNED BY
{{DESIGNED_BY}}
CHECKED BY
{{CHECKED_BY}}
JOB NO.
{{JOB_NO}}

## Slide 7
BESS PAD DETAILS — FOR PAGES PV0.2 & PV0.3
GENERAL NOTES:
1. STEM WALL SECTIONS WILL NEED TO BE FORMED AND POURED FIRST WITH A COLD JOINT WITH EXTENDED VERTICAL BARS TO TIE INTO THE SLAB. 2. GRAVEL BACKFILL WILL FOLLOW AFTER THE STEM WALLS ARE SET. 3. THE SLAB WILL BE PLACED AFTER THE BACKFILL. 4. REMOVE ALL TOP SOIL UNDER PERIMETER OF EQUIPMENT PADS. COMPACT NATIVE SOIL OR REMOVE ANY LOOSE MATERIALS. 5. INSTALLATION OF POST-INSTALLED ANCHORS (WEDGE ANCHORS, EPOXY ANCHORS) REQUIRE CONTINUOUS SPECIAL INSPECTION.
DESIGN CRITERIA:
2025 CBC, ASCE 7-22, ACI 318-19, ANSI/AWC NDS - 2024 Risk Category: {{RISK_CAT}} Wind Speed: {{WIND_SPEED}} mph, Exposure {{EXPOSURE}} Seismic Design Category {{SDC}}, Sds = 1.8 Bearing: 1500 psf, lateral bearing = 200 pcf for drilled piers Use f'c = 3000 psi, A615 Grade 60 rebar Break tests required at 7, 14 and 28 days. Max w/c = 0.5
S1.1 BESS PAD TOP VIEW (Static engineering drawing)
S1.1 BOLLARD DETAIL (Side view)
BESS PAD — SIDE VIEW See engineering drawing for dimensions. Slab: 12" thick, #4 @ 18" o.c. E.W. Stem walls: #4 @ 9" o.c. V&H Bearing: 1500 psf min. f'c = 3000 psi Standard hooks at bottom Gravel backfill, compact 6" lifts Cold joints at transitions
1 — BESS PAD DETAILS - TOP VIEW · SCALE: 1" = 2' 2 — SIDE VIEW · SCALE: 1" = 2' 3 — TYPICAL BOLLARD · SCALE: 1" = 1'
BOLLARD NOTES:
1. BOLLARDS IN REGULATION WITH CFC 312.2 2. REGULAR 84" POST — SCHEDULE 40 GALVANIZED STEEL PIPE. 3. DETAIL CONSIDERED MINIMUM FOR INSTALLATION. CARE WILL BE TAKEN TO CONFORM TO EXISTING BOLLARD AESTHETIC SUCH AS COLOR, END-CAP, OR REFLECTIVE VISIBILITY STRIPS. 4. REPAIRS, IF NECESSARY, SHALL BE MADE TO EXISTING FINISH GRADE AFTER BOLLARD INSTALLATION.
ClearSky
BUILDERS LLC
PO BOX {{GC_PO_BOX}}
{{GC_CITY}}, {{GC_STATE}} {{GC_ZIP}}
PH: {{GC_PHONE}}
PN - {{PROJECT_NAME}}
{{SITE_ADDR}}
{{CITY_SHORT}}, {{STATE}} {{ZIP}}
APN: {{APN}}
{{PERMIT_NO}}
REVIEWED FOR COMPLIANCE
{{AHJ_CITY}}
{{AHJ_DEPT}}
For {{PROJECT_NAME}} Subject to Code Compliance.
REVISIONS NEED REVIEW
DATE
REV
COMMENTS
{{ISSUE_DATE}}
00
ISSUE FOR PERMIT
S1.1
BESS PAD DETAILS
ISSUE DATE
{{ISSUE_DATE}}
REVISION DATE
{{ISSUE_DATE}}
DESIGNED BY
{{DESIGNED_BY}}
CHECKED BY
{{CHECKED_BY}}
JOB NO.
{{JOB_NO}}

## Slide 8
GEAR PAD DETAILS — INVERTER / TRANSFORMER / AC DISCONNECT
S1.2 GEAR PAD DETAILS (Top view, front view, side view, pier details)
1 — GEAR PAD TOP VIEW · SCALE: 1" = 1' 2 — FRONT VIEW · SCALE: 1" = 1' 3 — SIDE VIEW · SCALE: 1" = 1' 4 — PIER ELEVATION 5 — PIER PLAN VIEW
ClearSky
BUILDERS LLC
PO BOX {{GC_PO_BOX}}
{{GC_CITY}}, {{GC_STATE}} {{GC_ZIP}}
PH: {{GC_PHONE}}
PN - {{PROJECT_NAME}}
{{SITE_ADDR}}
{{CITY_SHORT}}, {{STATE}} {{ZIP}}
APN: {{APN}}
{{PERMIT_NO}}
REVIEWED FOR COMPLIANCE
{{AHJ_CITY}}
{{AHJ_DEPT}}
For {{PROJECT_NAME}} Subject to Code Compliance.
REVISIONS NEED REVIEW
DATE
REV
COMMENTS
{{ISSUE_DATE}}
00
ISSUE FOR PERMIT
S1.2
GEAR PAD DETAILS
ISSUE DATE
{{ISSUE_DATE}}
REVISION DATE
{{ISSUE_DATE}}
DESIGNED BY
{{DESIGNED_BY}}
CHECKED BY
{{CHECKED_BY}}
JOB NO.
{{JOB_NO}}

## Slide 9
GROUNDING DETAILS, SCHEDULE & TEST RECORD
S2.0 GROUNDING ELECTRODE DETAIL (XFMR / BESS / INVERTER)
NOTES:
1. SIZE OF CONDUCTORS SHALL COMPLY WITH CEC 250.94 2. BOND TO SEPARATE CONDUCTORS FROM INVERTER TO METAL BUILDING FRAME IF POSSIBLE (CEC 250.68) 3. GROUND TO METAL WATER PIPE EMBEDDED AT LEAST 10'-0" INTO THE SOIL IF AVAILABLE (CEC 250.68) 4. CHECK RESISTANCE TO GROUND. IF RESISTANCE EXCEEDS 25 OHMS, INSTALL ADDITIONAL GROUND RODS WITH CONDUCTORS AS SHOWN SEPARATED AT LEAST 6'-0" UNTIL RESISTANCE IS REDUCED TO 25 OHMS OR LESS (CEC 250.52). PROVIDE THIRD PARTY GROUND RESISTANCE TEST. 5. PROVIDE GAS AND WATER BOND (IF APPLICABLE).
GROUNDING SCHEDULE
CONDUCTOR
FROM
TO
SIZE
MATERIAL
INSULATION
NEC REF
EQUIPMENT GROUNDING CONDUCTOR
BESS / INVERTER
GROUNDING BUS
#{{WIRE_AWG}} AWG
Cu
Green/Bare
250.122
DC EQUIPMENT GROUNDING CONDUCTOR
PV / BESS
INVERTER
#{{WIRE_AWG}} AWG
Cu
Bare
690.45
GROUNDING ELECTRODE CONDUCTOR
GROUNDING BUS
GROUND ROD
#{{WIRE_AWG}} AWG
Cu
Bare
250.66
BESS CABINET BOND
—
—
Cu
—
—
250.118
FENCE BONDING JUMPER (TYP)
—
—
#6 AWG Cu min.
Cu (Bare)
—
IEEE 80
GROUND ROD (TYP)
—
—
5/8" Ø × 8'-0"
Cu-clad Steel
—
250.52(A)(5)
GROUND RING (IF REQ'D)
—
—
#2 AWG Cu min.
Cu (Bare)
—
250.52(A)(4)
GROUND RESISTANCE TEST RECORD (FIELD)
TEST ID
LOCATION
METHOD
RESULT (Ω)
PASS/FAIL
DATE
TECH
GR-1
XFMR Pad
3-Pt Fall of Potential
[ ]
[ ]
[ ]
[ ]
GR-2
BESS Pad
3-Pt Fall of Potential
[ ]
[ ]
[ ]
[ ]
GR-3
Fence Gate
Clamp-on
[ ]
[ ]
[ ]
[ ]
Note: All readings must be ≤25 Ω per NEC 250.53(A)(2), or a supplemental electrode must be installed.
S2.0 BESS GROUNDING DIAGRAM (Container grounding point diagram from manufacturer)
1 — GROUNDING ELECTRODE DETAIL: XFMR/BESS/INVERTER · SCALE: NTS 2 — DIAGRAM OF GROUNDING POINTS · SCALE: NTS
ClearSky
BUILDERS LLC
PO BOX {{GC_PO_BOX}}
{{GC_CITY}}, {{GC_STATE}} {{GC_ZIP}}
PH: {{GC_PHONE}}
PN - {{PROJECT_NAME}}
{{SITE_ADDR}}
{{CITY_SHORT}}, {{STATE}} {{ZIP}}
APN: {{APN}}
{{PERMIT_NO}}
REVIEWED FOR COMPLIANCE
{{AHJ_CITY}}
{{AHJ_DEPT}}
For {{PROJECT_NAME}} Subject to Code Compliance.
REVISIONS NEED REVIEW
DATE
REV
COMMENTS
{{ISSUE_DATE}}
00
ISSUE FOR PERMIT
S2.0
GROUNDING DETAILS
ISSUE DATE
{{ISSUE_DATE}}
REVISION DATE
{{ISSUE_DATE}}
DESIGNED BY
{{DESIGNED_BY}}
CHECKED BY
{{CHECKED_BY}}
JOB NO.
{{JOB_NO}}

## Slide 10
FENCING DETAILS — ISOMETRIC, PARKING LOT AND STREET VIEWS
S3.0 ISOMETRIC VIEW (Upload fencing isometric rendering)
S3.0 PARKING LOT VIEW (Upload fencing side view)
S3.0 STREET ELEVATION VIEW (Upload cross street elevation)
FENCING SCHEDULE
RUN
SIDE
LENGTH
HEIGHT
PANEL TYPE
A
Parking Lot
{{FENCE_LEN}}
8'-0"
B
Cross Street
{{FENCE_LEN}}
8'-0"
C
Property Line
{{FENCE_LEN}}
8'-0"
D
Gate
8'-0"
8'-0"
Double Swing
FENCING NOTES
Fence height: 8'-0" minimum measured from finish grade. Coordinate with local zoning and AHJ if greater height required. Posts: [2" × 2"] HDG steel tube. Set in [12" Ø] concrete footing, [36"] minimum depth below grade. Post spacing: [8'-0" o.c. typical], max [10'-0" o.c.]; reduce as required at gates and panel transitions. Concrete footing: f'c = [3,000] psi, crown above grade to shed water. Provide ground bonding jumper #6 AWG Cu between adjacent fence posts and to grounding electrode system per IEEE 80 and NEC 250. Gates: Provide one [double-swing 12'-0" wide] vehicle gate and one [pedestrian 4'-0"] gate. Gates to be self-closing & lockable per AHJ / IFC 1207. Signage on fence per E4.0 (Caution / Energy Storage / Emergency Contact). Maintain minimum [3'-0"] clearance from BESS enclosure to inside face of fence per NEC 110.26. Provide vegetation-free perimeter of [3'-0"] on both sides of fence; coordinate with landscape per local fire department requirements. All exposed fasteners: stainless or HDG. Tamper-resistant where accessible from public side. Coordinate fence location with property line survey and easements. Maintain {{SETBACK}} per local code.
1 — FENCING DETAILS — ISOMETRIC VIEW · SCALE: NTS 2 — PARKING LOT VIEW · SCALE: NTS 3 — CROSS STREET ELEVATION · SCALE: NTS
ClearSky
BUILDERS LLC
PO BOX {{GC_PO_BOX}}
{{GC_CITY}}, {{GC_STATE}} {{GC_ZIP}}
PH: {{GC_PHONE}}
PN - {{PROJECT_NAME}}
{{SITE_ADDR}}
{{CITY_SHORT}}, {{STATE}} {{ZIP}}
APN: {{APN}}
{{PERMIT_NO}}
REVIEWED FOR COMPLIANCE
{{AHJ_CITY}}
{{AHJ_DEPT}}
For {{PROJECT_NAME}} Subject to Code Compliance.
REVISIONS NEED REVIEW
DATE
REV
COMMENTS
{{ISSUE_DATE}}
00
ISSUE FOR PERMIT
S3.0
FENCING DETAILS
ISSUE DATE
{{ISSUE_DATE}}
REVISION DATE
{{ISSUE_DATE}}
DESIGNED BY
{{DESIGNED_BY}}
CHECKED BY
{{CHECKED_BY}}
JOB NO.
{{JOB_NO}}